## Slide 1
PRACTICAL GUIDE
FOR USING THE NG DetecTool DEVICE
THE PROCESS OF TESTING

## Slide 2: The advantages of the NG DetecTool
enables efficient patient treatment
prohibits further spread of ESBL and carbapenemase-producing bacteria
rapid and easy-to-use diagnostic system to detect ESBL and carbapenemases
in clinical samples:
direct detection of bacterial enzymes
responsible for ß-lactam resistance
2

## Slide 3: Slow isolation methods
Current methods take 16-32 hours and require cultured bacteria
3

## Slide 4: The rapid immunoassay test
New detection system: the workflow for detection of multidrug resistant bacteria is shortened to 20 - 30 min.
4
Workflow with NG DetecTool
Sample reception and processing
MDR bacteria detection / characterization
URINE
BLOOD CULTURE
RECTAL SWAB
No required incubation
2 min
overnight incubation
NGDETECTOOL 15 MINUTES

## Slide 5: Sample types, what they show and next steps
RECTAL SWAB
isolation of the patient
COLONIZATION
BLOOD
treatment of the patient
INFECTION
URINE
INFECTION
Samples taken from blood cultures positive with gram-negative bacteria
Samples positive for gram-negative bacteria
treatment of the patient
5
Notes: Mintavételi eszközök képeknek

## Slide 6
Key features of the NG DetecTool
  Concentrates bacteria from liquid sample
  Eliminates the interferences due to the biological media
  Improved sensitivity
  Decreases the time to result to 20-30 minutes. Please note, incubation is required for rectal swab samples (overnight), which extends the time to result.
6

## Slide 7
Lateral Flow immunoassay (LFIA) (Similar technology as a pregnancy test)
Detection process and features
Sample processing
B. Beta-lactamases Detection
Filtration
Extraction
Incubation
Deposition
  Single use
  No specific equipment
One device Two functions
ATTENTION: Please make sure you read the detailed NG DetecTool protocol before using the device on real-life samples.
7

## Slide 8
Membrane 0,2µm
Filtration part:
Filtration / Concentration
Upper part
Lower part
Cup
Detection system components 1
8

## Slide 9
Detection system components 2
Three main components
Cap/plunger
Cup
Tank
Membrane 0,2 µm
Processing part:
9

## Slide 10
Cassette
Strip
Test lines indicate the presence of enzymes responsible for the antibiotic resistance
Two main components
Detection part:
Detection system components 3
10

## Slide 11
Detection process – Sample preparation
This training material is a high-level overview on the operation of the device. ATTENTION: Please make sure you read the detailed NG DetecTool protocol before using the device on real-life samples.
BLOOD
URINE
Mix 2 volumes of positive blood culture with 1 volume of lysis buffer. Let react for minimum 2 minutes (possible up to 30’).
RECTAL SWAB
No preparation required
Inoculate transport medium of the swabs into Brain heart infusion media supplemented with cefotaxime for ESBL (CTXM) and ertapenem (for carbapenemases) and incubate overnight.
11
Notes: Mintavételi eszközök képeknek

## Slide 12
Sample
Sample volume ≤ 1,5 ml
Bacteria
1) Insert the cup into
the lower part
2) Add the sample
in the cup
3) Close the filtration system
with the upper part
4) Push the sample through the filter using a syringe full of air
Detection process – Filtration A
Sampling and filtration
12

## Slide 13
Sampling and filtration
3) Aspirate the desired volume of sample and some air with a syringe
4) Push the sample and
the air through the filter
Sample volume ≥ 1,5 ml
Bacteria
Detection process – Filtration B
1) Insert the cup into
the lower part
2) Close the filtration system
with the upper part
13

## Slide 14
Detection process – Extraction
Extraction and incubation
Bacteria
Labelled
antibodies
1) Remove the lower part
2) Transfer the cup in the tank and remove the upper part
14

## Slide 15
Detection process – Extraction
Extraction buffer
Labelled
antibodies
1) Remove the lower part
2) Transfer the cup in the tank and remove the upper part
3) Add 250 μl extraction buffer in the cup
4) Screw the cap
Extraction and incubation
14
5) Shake slightly the processing part (to conjugate the dissolution)

## Slide 16
Strip
Extracted sample
+
Labelled antibodies
Detection process – Detection
1) Place the processing part on the detection part
15

## Slide 17
Detection process – Detection
1) Place the processing part on the detection part
15
2) Break the bottom of the processing part by pressing it down
3) Read the result after 15 minutes

## Slide 18: Principle of the detection
Immunoassay:
antigene (analyte) – antibody reaction
Lateral Flow ImmunoAssay: the sample is applied at the end of the strip (sample pad), then migrates into the detection zone
Sample
Sample pad
Control line
Test line
Detection zone
Migration direction
Antibody
Labelled antibody
Enzyme (Antigen)
16

## Slide 19
The strip contains:
  a control line to confirm that the test is working properly
  testline(s) - ESBL(CTX-M) or carbapenemases (KPC, OXA, VIM, IMP, NDM)
Sample pad
Control line
CTX-M
KPC
OXA
VIM
IMP
NDM
Strip to ESBL
Strip to carbapenemases
Detection process – Detection
17

## Slide 20
Read the result after 15 minutes
The control line must be visible: when the control line does not appear, the test is invalid
Absence of a testline -> NEGATIVE
Presence of a testline -> POSITIVE
Detection process – Evaluation
18

## Slide 21
Actions to be taken 1
INFECTION
From blood / urine
COLONISATION
From rectal swab
Antibiotic treatment
When the result is positive
The patient must be placed in isolation
19

## Slide 22
Actions to be taken 2
Limited therapeutic options, consultation with infectious disease specialist
Positive result: consultation with infection control specialist is necessary
Antibiotic susceptibility test is required to adapt best therapy
20
Negative result for blood or urine sample:
  the sample may contain other resistant bacteria (except for the ESBL- and carbapenemase-producing bacteria)
  for haemoculture and urine, bacterial culture is required
Negative result for rectal swab:
no action required

## Slide 23: This is the end of the Principles of Testing Section of the NG DetecTool training Thank you for your attention!